## Slide 1: Required Reading ( From Lecture 1)
Michael E. Porter. How Competitive Forces Shape Strategy, Harvard Business Review, March-April 1979, pp. 137-145.(Search http://erms.library.cornell.edu/
Joseph L. Bower and Clayton M. Christensen. Disruptive Technologies: Catching the Wave, Harvard Business Review, January-February 1995, pp. 43-53. (Search http://erms.library.cornell.edu/)
Peter J. Denning and Ted G. Lewis. “Exponential Laws of Computing Growth.” Communications of the ACM. January 2017. ACM.org.

## Slide 2
Microprocessor Technology
&
Case Studies
NBAY 6120
March 03, 2020
Donald P. Greenberg
Lecture 2

## Slide 3: Semi-Conductor Technology and Economics
Required Reading:
  Craig R. Barrett. From Sand to Silicon: Manufacturing an Integrated Circuit, Scientific American, Special Issue, The Solid-State Century, January 1998, pp. 55-61. (Search: e-Journals/ Scientific American Archive Online/article (full text) http://www.library.cornell.edu/johnson/library/general/emba.html
  G. Dan Hutcheson and Jerry D. Hutcheson. Technology & Economics in the Semiconductor Industry, Scientific American, January 1996.

## Slide 4
Semi-Conductor Technology and Economics
Optional Reading:
  Mack, Chris. "The Multiple Lives of Moore's Law." IEEE Spectrum Apr. 2015: 30-37. Cornell University Library. Web. http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=7065415
Notes: G. Dan Hutcheson and Jerry D. Hutcheson. “Technology & Economics in the Semiconductor Industry, “ Scientific American: The Solid State Century, pp. 66-73, January 1996.

## Slide 5: Eniac 1946

## Slide 6: Super Computers
Control Data 1964
Cray 1990

## Slide 7
IBM 360 Model 75 (1965)
VAX-11/780 (1980)
Cray T3E (1995)
Cloud Computing (2010)
http://en.wikipedia.org
The line shows “Moore’s Law”: Transistor count doubles every two years.

## Slide 8: Transistor

## Slide 9: Shockley & the Traitorous Eight
William Shockley - Receives the Nobel Prize in Physics with Bardeen and Brattain (1956) leaves Bell Laboratory and forms Fairchild Semiconductor
Julius Blank - founded Xicor
Jean Hoerni - invented the planar process founded Amelco  Teledyne
Jay Last - founded Amelco  Teledyne
Sheldon Roberts - founded Amelco  Teledyne

## Slide 10: Shockley & the Traitorous Eight
Gordon Moore - founded Intel in 1968
Robert Noyce - founded Intel in 1968
Eugene Kleiner - founded Kleiner-Perkins
Victor Grinich - only a poor professor at UC Berkeley & Stanford

## Slide 11
From Sand to Silicon – Manufacturing an Integrated Circuit
Scientific American: The Solid-State Century, Special Issue 1998

## Slide 12: Chip Design

## Slide 13: Silicon Crystal

## Slide 14: Layering

## Slide 15: Masking & Etching

## Slide 16: Doping

## Slide 17: Interconnections & Dicing

## Slide 18: Probing Electrical Connections

## Slide 19: Dicing

## Slide 20: Chip Selection

## Slide 21: Chip Fabrication

## Slide 23: International Technology Roadmap for Semiconductors
Roughly 0.5 shrink every 3 years.
Intel released 22 nm chips in 2013

## Slide 24: Moore’s Law – CPU Transistor Counts
Processor | Transistor count | Date of introduction | Manufacturer | Process | Area
Intel 4004 | 2,300 | 1971 | Intel | 10 µm | 
Intel 8008 | 3,500 | 1972 | Intel | 10 µm | 
Intel 8080 | 4,500 | 1974 | Intel | 6 μm | 
Intel 8088 | 29,000 | 1979 | Intel | 3 μm | 
Intel 80286 | 134,000 | 1982 | Intel | 1.5 µm | 
Intel 80386 | 275,000 | 1985 | Intel | 1.5 µm | 
Intel 80486 | 1,180,000 | 1989 | Intel | 1 µm | 
Pentium | 3,100,000 | 1993 | Intel | 0.8 µm | 
AMD K5 | 4,300,000 | 1996 | AMD | 0.5 µm | 
Pentium II | 7,500,000 | 1997 | Intel | 0.35 µm | 
AMD K6 | 8,800,000 | 1997 | AMD | 0.35 µm | 
Pentium III | 9,500,000 | 1999 | Intel | 0.25 µm | 
AMD K6-III | 21,300,000 | 1999 | AMD | 0.25 µm | 
AMD K7 | 22,000,000 | 1999 | AMD | 0.25 µm | 
Pentium 4 | 42,000,000 | 2000 | Intel | 180 nm | 
Atom | 47,000,000 | 2008 | Intel | 45 nm | 
Barton | 54,300,000 | 2003 | AMD | 130 nm | 
AMD K8 | 105,900,000 | 2003 | AMD | 130 nm | 
Itanium 2 | 220,000,000 | 2003 | Intel | 130 nm | 
http://en.wikipedia.org/wiki/Transistor_count

## Slide 25: Moore’s Law – CPU Transistor Counts
Processor | Transistor count | Date of introduction | Manufacturer | Process | Area
Core 2 Duo | 291,000,000 | 2006 | Intel | 65 nm | 
AMD K10 | 463,000,000 | 2007 | AMD | 65 nm | 
AMD K10 | 758,000,000 | 2008 | AMD | 45 nm | 
Itanium 2 with 9MB cache | 592,000,000 | 2004 | Intel | 130 nm | 
Core i7 (Quad) | 731,000,000 | 2008 | Intel | 45 nm | 263 mm²
POWER6 | 789,000,000 | 2007 | IBM | 65 nm | 341 mm²
Six-Core Opteron 2400 | 904,000,000 | 2009 | AMD | 45 nm | 
Six-Core Core i7 | 1,170,000,000 | 2010 | Intel | 32 nm | 
Dual-Core Itanium 2 | 1,700,000,000 | 2006 | Intel | 90 nm | 596 mm²
Six-Core Xeon 7400 | 1,900,000,000 | 2008 | Intel | 45 nm | 
Quad-Core Itanium Tukwila | 2,000,000,000 | 2010 | Intel | 65 nm | 
Six-Core Core i7 (Sandy Bridge-E) | 2,270,000,000 | 2011 | Intel | 32 nm | 434 mm²
8-Core Xeon Nehalem-EX | 2,300,000,000 | 2010 | Intel | 45 nm | 684 mm²
10-Core Xeon Westmere-EX | 2,600,000,000 | 2011 | Intel | 32 nm | 512 mm²
Six-core zEC12 | 2,750,000,000 | 2012 | IBM | 32 nm | 597 mm²
8-Core Itanium Poulson | 3,100,000,000 | 2012 | Intel | 32 nm | 544 mm²
15-Core Xeon Ivy Bridge-EX | 4,310,000,000 | 2014 | Intel | 22nm | 541 mm²
62-Core Xeon Phi | 5,000,000,000 | 2012 | Intel | 22 nm | 350 mm²
Xbox One Main SoC | 5,000,000,000 | 2013 | Microsoft | 28 nm | 363 mm²
18-core Xeon Haswell-E5 | 5,560,000,000 | 2014 | Intel | 22 nm | 661mm²
IBM z13 Storage Controller | 7,100,000,000 | 2015 | IBM | 22 nm | 678 mm²
http://en.wikipedia.org/wiki/Transistor_count

## Slide 26: Why are we continuing to strive for smaller and smaller technology?
More transistors/chip  increased functionality and performance
Higher speeds  partially depends on how close together the components are placed
Cheaper – more chips/wafer, greater yields

## Slide 27
Yield Ratio

## Slide 28: Yield per Wafer

## Slide 29: Yield Ratio
Number of defects/unit area depends on the process
Total chips (nt) for a given wafer size is also inversely proportional to the chip area

## Slide 30: Size of Relative Contamination
..
Human Hair
Fingerprint
Smoke Particle
Slider

## Slide 31
Example:

## Slide 32
Can this Shrinking Technology Continue?

## Slide 33
Factors Contributing to Advancing Microprocessor Performance
Shrinking Component Size
Increasing Speed
Reducing Circuit Resistance
New Materials

## Slide 34
RISC vs. CISC
VLIW
Multi-level Cache
Parallelism & Pipelining
Factors Contributing to Advancing Microprocessor Performance

## Slide 35
RISC vs. CISC
VLIW
Multi-level Cache
Parallelism & Pipelining
Multi-core Technology
Factors Contributing to Advancing Microprocessor Performance

## Slide 36: Exponential Laws of Computing Growth
Dennings and Lewis, Jan. 2016

## Slide 37
International Technology Roadmap for Semiconductors
 | 2001 | 2004 | 2007 | 2010 | 2013 | 2016
Technology (nanometers) | 130nm | 90nm | 65nm | 45nm | 32nm | 22nm
Functions per Chip (millions) | 97 | 193 | 386 | 1546 | 3092 | 6184
Clock Speed (Ghz) | 2.5Ghz | 4.1Ghz | 9.3Ghz | 15Ghz | 23Ghz | 40Ghz
Wafer Size (millimeters) | 200mm | 300mm | 300mm | 300mm | 450mm | 450mm
Chip Size (mm2) | 140 mm2 | 14 0 mm2 | 140 mm2 | 140 mm2 | 140 mm2 | 140 mm2
Roughly 0.5 shrink every 3 years 29% cost/reduction/function/yr.

## Slide 38: Advanced Process Roadmap

## Slide 39: Moore’s Law – CPU Transistor Counts
Processor | Transistor count | Date of introduction | Manufacturer | Process | Area
Core 2 Duo | 291,000,000 | 2006 | Intel | 65 nm | 
AMD K10 | 463,000,000 | 2007 | AMD | 65 nm | 
AMD K10 | 758,000,000 | 2008 | AMD | 45 nm | 
Itanium 2 with 9MB cache | 592,000,000 | 2004 | Intel | 130 nm | 
Core i7 (Quad) | 731,000,000 | 2008 | Intel | 45 nm | 263 mm²
POWER6 | 789,000,000 | 2007 | IBM | 65 nm | 341 mm²
Six-Core Opteron 2400 | 904,000,000 | 2009 | AMD | 45 nm | 
Six-Core Core i7 | 1,170,000,000 | 2010 | Intel | 32 nm | 
Dual-Core Itanium 2 | 1,700,000,000 | 2006 | Intel | 90 nm | 596 mm²
Six-Core Xeon 7400 | 1,900,000,000 | 2008 | Intel | 45 nm | 
Quad-Core Itanium Tukwila | 2,000,000,000 | 2010 | Intel | 65 nm | 
Six-Core Core i7 (Sandy Bridge-E) | 2,270,000,000 | 2011 | Intel | 32 nm | 434 mm²
8-Core Xeon Nehalem-EX | 2,300,000,000 | 2010 | Intel | 45 nm | 684 mm²
10-Core Xeon Westmere-EX | 2,600,000,000 | 2011 | Intel | 32 nm | 512 mm²
Six-core zEC12 | 2,750,000,000 | 2012 | IBM | 32 nm | 597 mm²
8-Core Itanium Poulson | 3,100,000,000 | 2012 | Intel | 32 nm | 544 mm²
15-Core Xeon Ivy Bridge-EX | 4,310,000,000 | 2014 | Intel | 22nm | 541 mm²
62-Core Xeon Phi | 5,000,000,000 | 2012 | Intel | 22 nm | 350 mm²
Xbox One Main SoC | 5,000,000,000 | 2013 | Microsoft | 28 nm | 363 mm²
18-core Xeon Haswell-E5 | 5,560,000,000 | 2014 | Intel | 22 nm | 661mm²
IBM z14 Storage Controller | 9,700,000,000 | 2017 | IBM | 14 nm | 696mm²
32-core SPARC M7 | 10,000,000,000 | 2015 | Oracle | 20 nm | 
Centriq 2400 | 18,000,000,000 | 2017 | Qualcomm | 10 nm | 398 mm²
32-core AMD Epyc | 19,200,000,000 | 2017 | AMD | 14 nm | 4× 192 mm2
http://en.wikipedia.org/wiki/Transistor_count

## Slide 40: International Technology Roadmap for Semiconductors
 | 2001 | 2004 | 2007 | 2010 | 2013 | 2016
Technology (nanometers) | 130nm | 90nm | 65nm | 45nm | 32nm | 22nm
Technology (nanometers) | 2014 | 2016 | 2018 | 2019 | 2021 | 2024
 | 14nm | 10nm | 7nm | 5nm | 3nm | 2nm

## Slide 42: Semi-Conductor Technology and Economics
Required Reading:
  G. Dan Hutcheson and Jerry D. Hutcheson. Technology & Economics in the Semiconductor Industry, Scientific American, January 1996.

## Slide 44
A
B
C
Notes: G. Dan Hutcheson and Jerry D. Hutcheson. “Technology & Economics in the Semiconductor Industry, “ Scientific American: The Solid State Century, pp. 66-73, January 1996.

## Slide 45
Return on Investment (ROI)
Assumptions:
  Payback period (time)
  Net Present Value
    Value of future benefits in today’s money
  Internal Rate of Return
Notes: G. Dan Hutcheson and Jerry D. Hutcheson. “Technology & Economics in the Semiconductor Industry, “ Scientific American: The Solid State Century, pp. 66-73, January 1996.

## Slide 46
How do you predict what the technology, manufacturing cost, market demand, market supply, and competition will be five years in the future?

## Slide 47
Return on Investment (ROI) Model does not work well
Difficulties:
How long does the product last?
What is the price (revenue)/unit?
  Exponential change
  Non-linear pricing behavior
  Competition (monopoly pricing)
  Prediction of demand
  Technical obstacles
Notes: G. Dan Hutcheson and Jerry D. Hutcheson. “Technology & Economics in the Semiconductor Industry, “ Scientific American: The Solid State Century, pp. 66-73, January 1996.

## Slide 48: Profitability vs. Investment in the Computer Industry
Notes: G. Dan Hutcheson and Jerry D. Hutcheson. “Technology & Economics in the Semiconductor Industry, “ Scientific American: The Solid State Century, pp. 66-73, January 1996.

## Slide 49
Rising Profitability
Rising Investment
Profitability vs. Investment in the Computer Industry
D)
&
R
(including
profit
gross
cash
D
&
R
equipment
new
y
technolog
new
e
wher
year
previous
y
technolog
new
in
made
s
investment
year
during
generated
cash
ratio
by
Measured
=
+
=
=
Notes: G. Dan Hutcheson and Jerry D. Hutcheson. “Technology & Economics in the Semiconductor Industry, “ Scientific American: The Solid State Century, pp. 66-73, January 1996.

## Slide 50
1973
1974
1972
1975
1971
Profitability vs. Investment

## Slide 51: Profitability vs. Investment in the Computer Industry
It is obvious that with the shrinking technology, it is getting more expensive to move to the next generation process technology.
It is also obvious that the manufacturing cost as well as the sales price of processing chips is decreasing rapidly.

## Slide 52: Diminishing Profitability

## Slide 53
With these observations, what should the dominant chip manufacturers (Intel, IBM, TI, TSMC, Samsung, AMD, etc.) do?

## Slide 54: Instructions Per Second (IPS)
IPS = No. of cores x (No. of cycles/Sec.) x (Instructions/cycle)
Example: Digital Equipment Corporation
  VAX 11/780, 5Mhz
  Cost $250,000 1977
IPS = 1x5x10⁶(cycles/sec)x0.2(Instructions/cycle)
  =1x10⁶(Instructions)
  ⁖ The first 1.0 MIPS machine

## Slide 55: Instructions Per Clock-cycle per second (IPS) (Microprocessor CPU’S)

## Slide 56: Instructions Per Clock-cycle per second (IPS) (Microprocessor CPU’S)
Processor / System | MIPS and Frequency | (IPS / clock cycles per second) | (IPS / clock cycles per second / cores) | Year*
*Nvidia Ge-Force RTX-2080T.I | 76,000,000 MIPs at 1.5 GHz | 50,666.7 | 11.6 | 2019
*Nvidia Quadro RTX-2080T.I | 78,000,000 MIPS at 1.6 GHz | 48750.0 | 11.2 | 2019
*Nvidia DGX | 500,000,000 MFLOPs at 1.46 GHz | 357142.9 | 17.4 | 2017

## Slide 57: Impact of Changing Customer Demand

## Slide 58: Intel 2008
In 2008 the average selling price for all products continued to decline
The revenues for the mobility group as contrasted to the digital enterprise group continued to increase
Percentage of Revenue
(Dollars in Millions)
Intel 2008 Annual Report and 10-K, http://www.intc.com/annuals.cfm

## Slide 59: Intel Research and Development 2011

## Slide 60: Intel Capital Additions to Property, Plant and Equipment 2011

## Slide 61: Intel 2011
A new fab costs approximately $3-4B or more
Should Intel Continue to Invest In Creating New Fabrication Facilities?

## Slide 62: Intel Research & Development 2012

## Slide 63: Intel 2012

## Slide 64: Obama at Intel 2012

## Slide 65: Intel cancels 14nm Fab 42 in AZ, due to increasing competition from ARM
January 2014, ExtremeTech.com

## Slide 66
How did Intel maintain it’s revenue stream?
It Retrofitted two existing plants in Chandler Arizona
  22nm >>> 14 nm (Fab 22 & Fab 32)

## Slide 67: Is there another revenue stream?

## Slide 68: Intel 2015
Intel again delays 10nm technology. It will depend on revenue increase from Windows 10 and its new Skylake processor.
The second generation of 14nm production technology had significant yield improvements.
At the same time, Intel moved to purchase Altera so it could shift from PC’s to mobile devices.

## Slide 69: Intel’s $7B Investment
Wall Street Journal, Feb. 8th, 2017

## Slide 70: Intel 2018

## Slide 71
Will the cost of new fabrication plants lead to oligopolies in this industry?

## Slide 72
Fewer companies can deliver smaller and more powerful chips (July 20, 2009)
Chris Nuttall. “Moore’s Law hits economic limits,” FT.com, July 20, 2009 - http://www.ft.com/cms/s/0/01c8b5aa-754e-11de-9ed5-00144feabdc0.html

## Slide 73: Fewer companies can deliver smaller and more powerful chips July 20, 2009
Chris Nuttall. “Moore’s Law hits economic limits,” FT.com, July 20, 2009 - http://www.ft.com/cms/s/0/01c8b5aa-754e-11de-9ed5-00144feabdc0.html

## Slide 74: Cost of Current and Future FABs
TSMC invested $9.3 billion in its Fab15 300 mm wafer manufacturing facility in Taiwan.
Estimates are that future FABs might cost $20 billion

## Slide 75: Foundry Model
Many companies (Integrated Device Manufacturers, IDMs) design and manufacture integrated circuits (efficiency through vertical integration)
Today, there are many companies that:
  only design devices (fabless semiconductor companies),
  as well as merchant foundries that only manufacture devices.
The foundry model is a business vision that seeks to optimize productivity.
In 1987, the world’s first dedicated merchant foundry opened its doors: Taiwan Semiconductor Manufacturing Company (TSMC)
source: https://en.wikipedia.org/wiki/Foundry_model

## Slide 76: TSMC’s Customers
Manufacture’s chips for
  Qualcomm
  Nvidia
  Advanced Micro Devices (AMD)
  Broadcom, Altera
    (even some for Intel & Texas Instruments)
  Apple’s A5, A6 for iPad & iPhone
  Apple’s new A8
source: https://en.wikipedia.org/wiki/TSMC

## Slide 77: GlobalFoundries 2020
GlobalFoundries is an American Semi-Conductor Foundry in Santa Clara, CA, Vermont, Singapore, Germany, and owned by Advanced Technology Investment Company of the emirate of Abu Dhabi.
The firm manufactures chips for AMD, Broadcom, Qualcomm, and STMicroelectronics.
Wikipedia, GlobalFoundries

## Slide 78
“Every economic era is based on a key abundance and a key scarcity.”
George Gilder,
Forbes ASAP, 1992

## Slide 79
If processing is free what other options are available to create new revenue streams?

## Slide 80
“Watts are more important then MIPS or FLOPS”
- George Gilder
http://www.wired.com/print/gadgets/wireless/magazine/17-03/mf_netbooks

## Slide 81: ARM Holdings - Business Model
Shimpi, Anand Lal. "The ARM Diaries, Part 1: How ARM's Business Model Works.“ Anand Tech. N.p., 28 June 2013. Web. 31 Aug. 2015.

## Slide 82: ARM Holdings
Original name was Acorn Computers
In 1990 a new customer arrived, Apple: and company was renamed Advanced RISC Machines (ARM)

## Slide 83: ARM Holdings 2014
By 2014, ARM dominated the smartphone market and had the following market share
  95% smartphone market
  10% mobile market
  35% digital TV’s
  23% PC’s
In 2014 ARM cores were licensed for 12 Billion chips

## Slide 84: ARM’s Customers
Apple (iPhone 5, iPad, iPhone 5s, iPhone 6, etc.)
Samsung (Galaxy S4, S5, etc.)
Qualcomm (Snapdragon)

## Slide 85
In a fast moving technology, how do you market your product?
How do you get brand name recognition?
When do you start advertising?
Marketing & Advertising Strategies in the Computer Industry

## Slide 86
First major extension to x86 instruction set since 1985
57 new instructions to accelerate:
  2D & 3D graphics
  Video
  Speech synthesis and recognition
What is MMX?

## Slide 92: Four Commandments
Moore’s Law
Rock’s Law
Metcalfe’s Law
Wirth’s Law

## Slide 93
“Chip density doubles every 18 months.”
Processing Power (P) in 15 years:
Moore’s Law

## Slide 94: Moore’s Law (continued)
Original paper noted that the cost per electronic component was inversely proportional to the number of components/chip
In 1988 Erich Bloch (then head of IBM’s research division), later Chairman of NSF Board, & sponsor for Cornell’s Theory Center
“Moore’s law won’t work at feature sizes less than a quarter of a micron (250 nanometers)”
Moore, underestimated the staying power of photolithography, “No exponential trend lasts forever, but forever can be postponed”

## Slide 95: Rock’s* Law
“The cost of semiconductor tools will double every four years”
Actually this was not true and current cost is $3 – 4B (slightly more than in the1990’s)
What actually happened was:
  1980’s. . .increase in yield
  1990’s. . .increase in throughput
  (from 20 wafers/hr. 50 wafers/hr.)
  Now, reduced size with 193m stepper and larger wafers (300mm)
* Rock was an initial investor in Intel

## Slide 96: Metcalfe’s* Law
“The value of a network grows as the square of the number of users”
1980 - later in “There Oughta be a Law,” NY Times 1996
Unlike the previous laws, this can’t be quantified because value (what economists call utility) can’t be measured.
However, note the impact of search engines, and the business model of Google, Yahoo, etc.
* Inventor of the Internet standard

## Slide 97: Wirth’s* Law
“Software is slowing faster than hardware is accelerating”
IEEE Computer 1995
“Were it not for a thousand times faster hardware, modern software would be utter unusable”
Most of the features that bloated the programs were superfluous for most of the users most of the time
* Niklaus Wirth, Professor of ETH, Zurich and inventor of Pascal

## Slide 98
END. . .
Notes: G. Dan Hutcheson and Jerry D. Hutcheson. “Technology & Economics in the Semiconductor Industry, “ Scientific American: The Solid State Century, pp. 66-73, January 1996.