## Slide 1: Digital Photography
NBAY 6120
March 5, 2020
Donald P. Greenberg
Lecture 3

## Slide 2: Pinhole Camera
Note that the entire image through the pinhole is totally in focus on a single image plane.

## Slide 3: Focus Fundamentals

## Slide 5: Daguerre’s Early Photograph 1838

## Slide 6: Lincoln’s Daguerreotype 1860s

## Slide 7: Civil War Mathew Brady

## Slide 8: Kodak’s Early Camera 1888
from The Story of Kodak, Douglas Collins 1990, p. 57

## Slide 9
Color Film Paradigm Shift 1934
From multiple lenses or multiple exposures
to multiple layered film
The transition from the optical approach to the
chemical approach formed the new basis for
color photography
Mannes & Godowsky
1920’s

## Slide 10: Mannes & Godowsky 1930s
(The Story of Kodak, Douglas Collins p. 205)

## Slide 11
Protective Layer
Blue-sensitive Emulsion
Yellow Filter
Green-sensitive Emulsion
Interlayer
Red-sensitive emulsion
Foundation Layer
Acetate Base
Anti-halation Backing
(fig. 1.6, Color Photography, Robert Hirsch, p. 5)

## Slide 12: Old Way – Mail film and receive prints 1940s

## Slide 13: Polaroid Land Camera 1947

## Slide 14
(Charge-Coupled Devices for Quantitative Electronic Imaging, 1991 Photo-metrics, Ltd. p. 6)
Photo-detector Technology

## Slide 15
CMOS Technology
Complementary metal oxide semiconductor
Follows the semiconductor industry cost curves
Processing (which is “free”) can perform calculations on each pixel within frame time (e.g. correct for lighting, motion blur, etc.).

## Slide 16: Silver Halide
Paul R. Montague. “Digital Imaging Comparing Film with Digital Images,” The Ophthalmic Photographers’ Society, Inc. http://www.opsweb.org/Op-Photo/Digital/DigImage1.htm
A low speed, ISO 32 film produces this fine grained image. The right image is a small portion of the whole negative on the left.
A high speed, ISO 400 film produces a coarser grain with less apparent sharpness in the image.

## Slide 17: Silver Halide Crystals
Is this analog or digital?

## Slide 18
$14,000 approximately, June 1994
Bayer Pattern 1994

## Slide 19: Kodak DCS 460
1995 – the highest resolution digital camera ($35,600)
2000 – price had dropped to $2,500

## Slide 20: PROFESSIONAL Digital Cameras 2014
Nikon Digital SLR
16.2 MegaPixels
$5,999
Canon EOS 5DSR
50.6 MegaPixels
$3,899

## Slide 21: When is a phone not a phone?
…when it’s a camera...

## Slide 22: iPhone 8 & 8+ Fall 2017 Release 9/12/17
Basic chip – 6 processors
  2 performance + 4 efficiency
  GPU
  4.3 B transistors
  10nm technology
2 – 12mp cameras
Wireless charging
Applications
  A/I
  Machine learning
  Face recognition
  Augmented reality

## Slide 23: Extreme Imaging Pixel Camera, 9/15/2016
Marc Levoy

## Slide 24: Extreme Imaging Pixel Camera, 9/15/2016
Marc Levoy

## Slide 25: Magritte’s The Empire of Light II 1950

## Slide 26: Pixel Night Sight 2018
Marc Levoy. “Night Sight: Seeing in the Dark on Pixel Phones”

## Slide 27: Pixel Night Sight 2018
Marc Levoy. “Night Sight: Seeing in the Dark on Pixel Phones”

## Slide 28: Advanced Digital Photography

## Slide 29: Vergence-Accommodation Conflict

## Slide 30: Pixel 2 Phase Detection for Depth Mapping 2018
Marc Levoy. “Portrait mode on the Pixel 2 and Pixel 2 XL smartphones”

## Slide 31: Autofocus by Phase Detection
Marc Levoy and Nora Willet. “Autofocus: phase detection”

## Slide 32: Pixel 2 Phase Detection for Depth Mapping 2018

## Slide 33: AWARE-2
http://www.kickstarter.com/projects/aqueti/carolina-zoomin

## Slide 34: Eye of a Fly AWARE-2 Duke University
http://www.nanowerk.com/spotlight/spotid=3744.php

## Slide 35
http://gigapan.com/galleries/11088/gigapans/146504

## Slide 36: AWARE-2
http://www.kickstarter.com/projects/aqueti/carolina-zoomin

## Slide 37: Gigapixel Images Prof. Pedro Sander HKUST
2010

## Slide 38
http://gigapan.com/gigapans/58857

## Slide 39: Canon’s 250-megapixel camera sensor 09/08/15
Can read letters 11 miles away!

## Slide 40: World’s Largest Digital Camera 2018
“The Largest Digital Camera in the World Takes Shape”
npr.org
Large Synoptic Survey Telescope
Biomimicry

## Slide 41: Light Field Photography
Images are not two dimensional!

## Slide 42: Quantifying Illumination
Irradiance
Radiance is defined as the light energy coming
from a specific direction.
Radiance
Irradiance

## Slide 43: What is a Light Field?
Radiance is defined as the light energy coming from a specific direction.
A light field is defined as the radiance at a position (x, y), and a direction (θ, φ).
Thus, the light field is a 4-dimensional space.

## Slide 44: Light Field
A light field can be represented by four variables L(u,v,s,t)

## Slide 45: Light Field

## Slide 48: Multi-camera array and LF camera are duals

## Slide 49: Key LF-camera advantage: a single lens
(more familiar, reduces complexity, simplifies calibration, …)

## Slide 50: Lytro Camera 2015

## Slide 51: Lytro Camera 2015

## Slide 54: Lytro’s last light field camera 2017

## Slide 55: End

## Slide 56: Computer Graphics Software & Hardware
NBAY 6120
Lecture 3
Donald P. Greenberg

## Slide 57: Ivan Sutherland 1963

## Slide 58: General Electric 1967
Program of Computer Graphics, Cornell University

## Slide 59: Cornell in Perspective Film 1972
Program of Computer Graphics, Cornell University

## Slide 61
Gouraud Thesis
Gouraud Flat Polygon Shading 1972
Each polygon is shaded based on a single normal.

## Slide 62
Gouraud Thesis
Gouraud Smooth Shading 1972
Each pixel is shaded by interpolating intensities computed in each of the polygon’s vertices.

## Slide 63: Phong Shading 1974

## Slide 64: Direct Illumination Pipeline

## Slide 65: Model
Environment
  Geometry & topology
  Material Properties
    Color, reflectance, textures
    (Cost, strength, thermal properties)
Lighting
  Geometry & position
  Intensity, spectral distribution
  Direction, special distribution

## Slide 66: Camera
Viewer position
Viewer direction
Field of View
  Wide angle
  Telephoto
Depth of focus
  Near
  Far

## Slide 67: Perspective Transformation
Perspective Transformation
  Matrix multiplication (4 x 4)
Clipping objects outside the field of view
Culling back-facing surfaces

## Slide 69: Brunelleschi’s Experiment

## Slide 70: Hidden Line Algorithm

## Slide 71: Hidden Line Algorithm

## Slide 72: Seurat 1884-1886

## Slide 73: Micrograph of TV Phosphors 1950’s

## Slide 74: Raster Operations
Conversion from polygons to pixels
  Color computation
Hidden surface removal (z-buffer)

## Slide 75
Typical frame buffer
  1280 x 1024 pixels
  3 channels (red, green, blue)
  1 byte/channel
Total memory
  3 3/4 megabytes - single buffer
  7 1/2 megabytes - double buffer
Image Storage

## Slide 76: E & S Frame Buffer 1975

## Slide 77: Display
Digital to analog conversion
  1280 x 1024 resolution
  60 frames/second
Total data rate
  1 ¼ million pixels
  x 3 bytes/pixel
  x 60 frames/second
  = 225 megabytes/second
  = 1.8 gigabits/second

## Slide 78: Refresh vs. Update Rate
The “refresh rate” is the number of times per second the entire image is drawn
The “update rate” is the number of times per second the image is changed

## Slide 79: Temporal Properties of NTSC
low refresh rate -> flicker
high refresh rate -> too much bandwidth
solution: interlacing
provides 60 Hz refresh rate with only 30 Hz update rate
field 2
field 1
field 3
field 4
frame 2
frame 1
REFRESH

## Slide 80: Update Rate vs. Refresh Rate
Film: 24fps update rate, 3 blade shutter, 72Hz refresh rate
Video: 30fps update rate, 2:1 interlacing, 60 Hz refresh rate
interlacing: matches flicker limits of vision, minimizes bandwidth

## Slide 81: Direct Illumination

## Slide 82: Phong Model: Variations of Specular Exponent
Roy Hall

## Slide 83: Reflection Descriptions
Images weren’t realistic
  Poor material representations
  Lack of global illumination
Need to measure how light reflects
Need to derive algorithms to compute global illumination

## Slide 84: Light Measurement Laboratory
Notes: Such a laboratory is not cheap, this one has about 1/2Meg of equipment, from corporate sponsors like HP and Kodak, and government grants
Purpose of the LML is to develop databases and provide reference measurements for the computer graphics community.
Next slide

## Slide 85: Reflectance Three Approximate Components
Ideal diffuse (Lambertian)
Directional
diffuse
Ideal
specular

## Slide 86: Cook-Torrance Renderings 1979

## Slide 87: The Geometry of Scattering from a Layered Surface
acm Computer Graphics, Siggraph 1993 p. 166

## Slide 88
Henrik Wann Jensen, Stephen R. Marschner, Marc Levoy, Pat Hanrahan. “A Practical Model for Subsurface Light Transport,” ACM Siggraph 2001, August 2001, Los Angeles, CA, pp. 511-518.

## Slide 89: Schematic Model of the Image Process
acm Transactions on Graphics, Siggraph 2003 p. 773

## Slide 91: Direct Lighting and Indirect Lighting
9
9
9
9
7
6
6
9
9
7
3
3
3
9
9
14
1
1
1
7
7
9
7
7
5
5
7
9
9
9
5
5
5
7
9
9
5
5
5
7
9
9
6
6
9
9
9
9
7
9
9
9
9
7
6
6
9
9
7
3
3
3
9
9
14
1
1
1
7
7
9
7
7
5
5
7
9
9
9
5
5
5
7
9
9
5
5
5
7
9
9
6
6
9
9
9
9
7
Direct
Indirect
Direct

## Slide 92: Direct Lighting Only

## Slide 93: Global Illumination

## Slide 94: Global Illumination Algorithms
Ray Tracing
Radiosity

## Slide 96: Ray Tracing Eric Haines 1985

## Slide 97: Radiosity 1984

## Slide 98: Radiosity Eric Chen 1986

## Slide 99: Rendering Framework 1997

## Slide 100: Surface Reflectance

## Slide 101: Ray Tracing

## Slide 103: Path Tracing
Path Tracing is similar to ray tracing except that many more rays are sent for each pixel.
Rays are sent out on a probabilistic basis depending on the reflectance (transmittance) distributions of each surface that is struck.
Computations can be accelerated by using “importance sampling”, where the ray directions are dependent on the magnitude of the potential effects.

## Slide 104: Bi-directional Path Tracing
Photograph

## Slide 105: Graphics Pipeline Hardware
“Moore's Law is for wimps.”

## Slide 106: Why a Pipeline?
A pipeline allows multiple processes to occur in parallel.
Example: Automobile assembly line.
  Assume 4 stations, each taking 2 minutes to do its task. It takes 8 minutes to make a car, but the rate at which cars are made is one every 2 minutes.

## Slide 107: Example: Automobile Pipeline
Automobile takes 8 minutes to make, but the assembly line makes a car every two minutes.
Build
frame
Add
engine
Add
windows
Paint
body
2 minutes 2 minutes 2 minutes 2 minutes

## Slide 108: Example: Automobile Pipeline
Automobile takes 8 minutes to make, but the assembly line makes a car every two minutes.
Build
frame
Add
engine
Add
windows
Paint
body
2 minutes 2 minutes 2 minutes 2 minutes
A
B
C
D
E
A
B
C
D
A
B
C
A
B
Stage 1
Stage 2
Stage 3
Stage 4
Time (minutes)
0
2
4
6
8
10
® Donald P. Greenberg - Cornell Program of Computer Graphics

## Slide 110: Graphics Hardware circa 1970
System used to generate Phong goblet

## Slide 111: Graphics Hardware circa 1986
Added Z-Buffer
Added Double Frame Buffer
Rasterization and visible surface computations performed in hardware

## Slide 112: Multipass Example: Light Maps
Two separate textures, one for the material’s composition, one for the lighting
X
=
J.L.Mitchell, M. Tatro, and I. Bullard

## Slide 113: Castle’s Geometry
Agata & Andrzej Wojaczek, Advanced Graphics Applications Inc.

## Slide 114: Reflection Example - Castle
Agata & Andrzej Wojaczek, Advanced Graphics Applications Inc.

## Slide 115: Graphics Pipeline 1980s
M
L
P
S
D
V
M — Model
L — Lighting
P — Perspective/Clipping
S — Scan Conversion/Z-buffer
D — Display Storage
V — Video
® Donald P. Greenberg - Cornell Program of Computer Graphics

## Slide 116: Graphics Hardware 2003
Early GPU’s performed lighting and clipping operations on locally stored model

## Slide 117: Graphics Pipeline 2003 +
® Donald P. Greenberg - Cornell Program of Computer Graphics

## Slide 118: Graphics Hardware 2009

## Slide 119: Moore’s Law – GPU Transistor Counts
Processor | Transistor count | Date of introduction | Manufacturer | Process | Area
R520 | 321,000,000 | 2005 | AMD | 90 nm | 288 mm²
R580 | 384,000,000 | 2006 | AMD | 90 nm | 352 mm²
G80 | 681,000,000 | 2006 | NVIDIA | 90 nm | 480 mm²
R600 Pele | 700,000,000 | 2007 | AMD | 80 nm | 420 mm²
G92 | 754,000,000 | 2007 | NVIDIA | 65 nm | 324 mm²
RV790XT Spartan | 959,000,000 | 2008 | AMD | 55 nm | 282 mm²
GT200 Tesla | 1,400,000,000 | 2008 | NVIDIA | 65 nm | 576 mm²
Cypress RV870 | 2,154,000,000 | 2009 | AMD | 40 nm | 334 mm²
Cayman RV970 | 2,640,000,000 | 2010 | AMD | 40 nm | 389 mm²
GF100 Fermi | 3,200,000,000 | Mar 2010 | NVIDIA | 40 nm | 526 mm²
GF110 Fermi | 3,000,000,000 | Nov 2010 | NVIDIA | 40 nm | 520 mm²
GK104 Kepler | 3,540,000,000 | 2012 | NVIDIA | 28 nm | 294 mm²
Tahiti RV1070 | 4,312,711,873 | 2011 | AMD | 28 nm | 365 mm²
GK110 Kepler | 7,080,000,000 | 2012 | NVIDIA | 28 nm | 561 mm²
RV1090 Hawaii | 6,300,000,000 | 2013 | AMD | 28 nm | 438 mm²
GM204 Maxwell | 5,200,000,000 | 2014 | NVIDIA | 28 nm | 398 mm²
GM200 Maxwell | 8,100,000,000 | 2015 | NVIDIA | 28 nm | 601 mm²
Fiji | 8,900,000,000 | 2015 | AMD | 28 nm | 596 mm²
GP102 Pascal | 12,000,000,000 | 2016 | Nvidia | 12 nm | 471 mm²
Vega 10 | 12,500,000,000 | 2017 | AMD | 14 nm | 484 mm²
GP100 Pascal | 15,300,000,000 | 2016 | Nvidia | 16 nm | 610 mm²
GV100 Volta | 21,100,000,000 | 2017 | Nvidia | 12 nm | 815 mm²
http://en.wikipedia.org/wiki/Transistor_count

## Slide 120: Instructions Per Clock-cycle per second (IPS) (Microprocessor CPU’S)

## Slide 121: Instructions Per Clock-cycle per second (IPS) (Microprocessor CPU’S)
Processor / System | MIPS and Frequency | (IPS / clock cycles per second) | (IPS / clock cycles per second / cores) | Year*
*Nvidia Ge-Force RTX-2080T.I | 76,000,000 MIPs at 1.5 GHz | 50,666.7 | 11.6 | 2019
*Nvidia Quadro RTX-2080T.I | 78,000,000 MIPS at 1.6 GHz | 48750.0 | 11.2 | 2019
*Nvidia DGX | 500,000,000 MFLOPs at 1.46 GHz | 357142.9 | 17.4 | 2017
Microprocessor GPU’S

## Slide 122: Integrated Graphics
All mobile microprocessor manufacturers (Intel, AMD, Qualcomm, etc.) have recently been integrating graphics hardware on to their chips.
Will this be a disruptive technology to Nvidia?

## Slide 123: Intel – Integrated Graphics 2013

## Slide 124: AMD – Integrated Graphics 2013

## Slide 125: AMD – Integrated Graphics 2014
“Kaveri”
28 nm
47% GPU
47% GPU

## Slide 126: Intel’s Ice Lake 2019

## Slide 127: End. . .