## Slide 1: Networks, History, Bandwidth and Compression
NBAY 6120
Lecture #4
March 10, 2020
Dr. Donald P. Greenberg

## Slide 2: Required Reading
“Uncle Sam, Ma Bell and Her Babies: A Timeline,” The New York Times. December 22, 1994. Barbara Kantrowitz. The Birth of the Internet, Newsweek, August 8, 1994, vol. 124, Is. 6, pg. 56.

## Slide 3: Recommended Reading
Klint Finley. “Tech Giants to Join Legal Battle Over Net Neutrality,” January 5, 2018. Wired

## Slide 4: Comparison between auditory and visual sensory systems
The human auditory channel is serial.
    All of the different frequencies are condensed into a single channel at a given point in time.
The human visual system is parallel.
    Many pieces of information (e.g. electrical impulses, pixels) are received at the same time.
Both systems are time dependent.

## Slide 6: Pictorial Data vs. Text
Text
1 character = 8 bits
1 word = 8 characters 2.4 Kilobytes
1 page = 300 words
Picture
1280 x 1024 x 3 bytes/pixel = 3 ¾ Mbytes

## Slide 7: Dynamic Information (Bandwidth Required)
Voice 44,000 bits/second
Video 512 x 480 x 8 bits x 30 fps = 7 1/2 Mbytes/second = 60 Mbits/second (1363x)
HDTV 1920 x 1280 x 3 bytes x 60fps = 420 Mbytes/second (76,328x)
* Statistics represent uncompressed data.

## Slide 8: History Of The Internet ARPA Team

## Slide 9: Internet - History & Growth Chronology
1973 - Vinton Cerf & Robert Kahn - designed Internet architecture based on TCP/IP
1979 - Configuration Control Board - contracted parts of infrastructure
1980 - U.S. Department of Defense - adopted TCP/IP,
MILNET designed to withstand atomic attack - becomes
ARPANET
Early 1980’s - ARPANET becomes known as Internet
researchers enticed to use CSNet (paid by NSF)

## Slide 10: Internet - History & Growth Chronology cont’d
1983 - TCP/IP - becomes standard
1990 - ARPANET - decommissioned and replaced by NSFNet backbone
NSF -expands network to other research communities
1993 - NSF -no longer provides funding for NSFNet backbone
NAP’s (network access points) established in four cities

## Slide 11
Circa 1993

## Slide 12: Internet - History & Growth Chronology cont’d
1993 - Mosaic - Introduced by University of Illinois
(Marc Andreesen)
1994 - NSF -links four national supercomputer centers at
155 Mbs (bandwidth to approach 2.5 Gbs)
contracts MCI to link other sites
Internet - opens to commercial usage
1994 - Netscape - formed by Jim Clark

## Slide 13: Uncle Sam, Ma Bell And Her Babies: A Timeline
1982 - AT & T and the Department of Justice signed consent decree.
• AT & T divests its 22 local Telco’s
• AT & T can enter previously restricted arenas
• Baby Bell’s prohibited from manufacturing equipment and offering long distance services. They cannot provide content

## Slide 14: Uncle Sam, Ma Bell And Her Babies: A Timeline
1984 - The AT & T divestiture takes effect.
1987 - The F.C.C. scraps rules that limit phone company profits.
1988 - Judge Greene agrees to let the Bells offer voice mail and E- mail services, and transmit electronic publishing for others, but not provide content.

## Slide 15: Con’t: Uncle Sam, Ma Bell And Her Babies: A Timeline
1989 - A seven-year ban on AT & T’s entry into electronic publishing is allowed to lapse.
1991 - Judge Greene removes the information services restriction from the Bells, but leaves in place the rules against manufacturing and long- distance service.
1993 - A Federal court in Virginia lifts for Bell Atlantic the video programming ban contained in the Cable Television Act of 1984.

## Slide 16: Con’t: Uncle Sam, Ma Bell And Her Babies: A Timeline
1994 - The House overwhelmingly approves legislation's that would let the Bells make equipment and enter the cable and long-distance business in return for accepting competition in their local telephone markets.
• A comparable Senate bill collapses - too much competition for the cable and long-distance companies.
1995 - The Senate passes a bill to overhaul communications regulation.
• The House passes a communications bill that is similar to the Senate version.
1996 - New Telecommunication bill passed February 1, 1996

## Slide 17: The Telecommunication Bill of 1996

## Slide 18: What The Telecommunication Bill Will Do
LONG-DISTANCE PHONE SERVICE
Seven regional Bell’s can enter into the long-distance phone business, must open their local phone networks
LOCAL PHONE SERVICE
Local phone markets open to new competitors (AT & T, MCI and cable TV companies) without specifying how much they pay

## Slide 19: What The Telecommunication Bill Will Do
BROADCAST
Raises the national TV-station ownership cap. Requires TV sets to block violent or sexual programs.
CABLE
Lifts all rate regulations in three years for big cable systems.

## Slide 20: What The Telecommunication Bill Will Do
INTERNET
Transmission of indecent material is a crime without restricting minor’s access.
SPECTRUM
TV Stations get valuable new broadcast spectrum for advanced TV free of charge. (To be revisited)

## Slide 21: How Did We Get Into This Mess?

## Slide 22: Level 3 Map 2012

## Slide 23: Submarine Cable Map 2018
https://www.submarinecablemap.com/

## Slide 24: MAREA Facebook & Microsoft

## Slide 25: Google & Amazon Transpacific Submarine Cable

## Slide 26: Network Typologies
Wired Networks –
Copper wires (telephone companies, DSL)
Fiber/coaxial cables
(cable television companies)
Fiber to the home (everybody)
Wireless Networks –
Satellites
Hybrid Networks –

## Slide 27: Wired Technology

## Slide 28: What is the current bandwidth of a single channel of coaxial cable?
One NTSC TV channel
512 x 512 x 8 bits/pixel x 30fps = 7.5MBs = 60 Mbs
One coaxial cable can carry 256 channels
 Theoretically, one coaxial cable has lots of bandwidth
Assuming one-half is used for digital information,
e.g. 128 x 60 Mbs = 7.68 Gbs (shared)

## Slide 29: The Architecture of a Hybrid Fiber-Coaxial Network
1 - Content transferred from the Internet to the fiber-optic backbone.
2 - The Network Operations Center (NOC) monitors the network, using data from cable modems.
3 - A regional data center caches copies of frequently requested content.

## Slide 30: The Architecture of a Hybrid Fiber-Coaxial Network
4 - Information is relayed by fiber optics (red) to “head ends.”
5 - Each fiber node connects to coaxial cable (blue) that links about 1,000 homes.
6 - A cable modem in the home decodes that user’s data.
7 - A home office may have a splitter sending the TV signals to a TV and the data to a cable modem.

## Slide 31: Coaxial Cable Network

## Slide 32: Fiber Optic Cable Network

## Slide 33: Advantages of Optical Fiber
High bandwidth capacity
Light within fiber can be “bent”
Cheap and abundant raw material
Low signal deterioration reducing need for amplification
Multichannel capacity (WDM)

## Slide 35: Frequency Spectrum

## Slide 36: Internet Ping Times Stanford - MIT

## Slide 37
Ping Test Link

## Slide 38: Wireless Coding Technologies

## Slide 39: First Generation (Analog)
Early 1980’s - 2000
AMPS (Advanced Mobile Phone System)
FDMA (Frequency Division Multiple Access)
Scientific American Oct. 2000

## Slide 40
Scientific American Oct. 2000

## Slide 41
Scientific American
Oct. 2000

## Slide 42: Second Generation (Digital)
Early 1990’s - 2000
TDMA (Time Division Multiple Access)
Original GSM (Global System for Mobile Communication)

## Slide 43
Scientific American
Oct. 2000

## Slide 44: Second Generation (Digital)
Early 1990’s - 2000
TDMA (Time Division Multiple Access)
Original GSM (Global System for Mobile Communication)
CDMA (Code Division Multiple Access)
PCS (Personal Communications Service)

## Slide 45
Scientific American
Oct. 2000

## Slide 46: Third Generation (Broadband) 1991-2000
W-CDMA (Wideband Code Division Multiple Access)
Refinement of CDMA technology
Minimum data rate for stationary users is 2Mbs
Scientific American Oct. 2000

## Slide 47: What is 4G?
Introduced in 2012.
4G is an entirely IP based technology using internet protocols and is the approximately 10x 3G.
The goals included enhanced security measures, mobile technology, and a smoother transition of data when a device moves across areas covered by different networks.
Specifications include peak data rates, latency, spectrum efficiency, etc.

## Slide 48: What is 4G?
The IP telephony includes ultra-broadband internet access, gaming services, and Internet TV, and at least 100Mbs when client is moving at high speeds and 1 Gbs when the client is stationary.

## Slide 49: Wireless Technology Progression
Emerging Wireless Technologies, http://www.safecomprogram.gov/NR/rdonlyres/5C74C631-ACF6-433F-B313-C04D041A5489/0/Look_Future_Wireless_Communications_Beyond3G.pdf

## Slide 50: The Negroponte Switch
1990’s Voice communication sent through wires
      Video programs sent through air
2010  Voice communication sent through air
Video programs sent through cable
Note the exception: Satellite direct broadcast TV
Gilder Report

## Slide 51: 5G Technologies 2018
Bloomberg Businessweek, August 2017

## Slide 52: 5G Goes for the Gold February 2018
Korea telephone announced plans to demonstrate 5G
(100x with delays < 1ms) at the winter Olympics
Anticipated to be available in 2019
IEEE Spectrum, January 2018

## Slide 53: Global Consumer Internet Traffic

## Slide 54: Prediction of Demand Cisco
Globally, mobile data traffic will increase sevenfold between 2016 and 2021
The number of devices connected to IP networks will be three times as high as the global population in 2021
Traffic from wireless and mobile devices will account for more than
63 percent of total IP traffic by 2021

## Slide 55: Prediction of Demand Cisco 2017-2022
Globally, IP video traffic will be 82 percent of all consumer Internet traffic by 2022, up from 73 percent in 2016.
Virtual reality and augmented reality traffic will increase 20-fold between 2016 and 2021, at a CAGR of 82 percent
Forecast and Trends, Cisco 2017-2022

## Slide 56: Data explosion vs. bandwidth?
Which will grow faster?
The problem is that wireless bandwidth is limited!

## Slide 58: Compression Technology

## Slide 59: Why Compress ?
Space requirement (storage)
Bandwidth requirements (channel width)
Time requirement (latency)

## Slide 60: How to Compress?
Color Fidelity
Redundancy
Accuracy
  Lossless
  Lossy

## Slide 61: Biconical Color Solid
George Joblove

## Slide 62
Figure 12.1– Foundations of Sensation and Perception, George Mather
Opponent Color Theory

## Slide 63: Biconical Color Solid
George Joblove

## Slide 64: Opponent Color Theory Hering 1892
There are three types of color receptive fields called opponent channels.
Black – White (luminance) channel M + L
Green – Red channel M - L
Yellow – Blue channel M + L - S

## Slide 65
Four particular colors appear to be “unique”.
  Red, Green, Blue, and Yellow
He considered these to be the “cardinal directions” of chromaticity
All other colors seem to be intermediate between these four
Opponent Color Theory Hering 1892

## Slide 66
Channel | Combination | Resolution
black - white | M + L | very high
Green - red | M – L | High
yellow - blue | M + L – S | low
Opponent Color Theory Hering 1892

## Slide 67
Cones interconnect in the retina, eventually leading to opponent-type signals.
Roy S. Berns. “Billmeyer and Saltzman’s Principles of Color Technology, 3rd Ed. 2000, John Wiley & Sons, Inc. p. 16.
Opponent Color Theory

## Slide 68: Opponent Color Theory Hering 1892
Figure 12.9– Foundations of Sensation and Perception, George Mather

## Slide 69
Image from “Eye, Brain, and Vision,” David Hubel, 1988

## Slide 70: Full Color Image
YIQ http://en.wikipedia.org/wiki/YIQ

## Slide 71: Luminance Image (Y)
YIQ http://en.wikipedia.org/wiki/YIQ

## Slide 72: Color Addition (Red/Green Axis)(I)
YIQ http://en.wikipedia.org/wiki/YIQ

## Slide 73: Color Addition (Yellow/Blue Axis)(Q)
YIQ http://en.wikipedia.org/wiki/YIQ

## Slide 74
Heidi YIQ

## Slide 75
Heidi YIQ

## Slide 76
Morse Code

## Slide 80: Lossless Compression System
Original
Data (X)
Lossless
Encoder
Decoder
Decompressed Data = Original Data.
Original
Data (X)
Compressed
Data

## Slide 81: When is Lossless Compression Needed?
Medical – patient diagnosis
Aerial photography – surveillance
High quality art and photo reproduction
Legal evidence
Augmented Reality

## Slide 82: Lossless Compression Methods
Run Length Codes
Huffman Codes
Lempel-Ziv Codes
Notes: In a memory-less code, each sample in the data-vector to be encoded is replaced by a code-word from a prefix set of bit-strings.
Huffman encoding gives an efficient way to find an optimal Kraft vector L for the given frequency vector F such that L.F is minimized.
  Entropy Bounds : Let R(X) be the compression rate in code-bits per data sample arising from the encoding of the data vector X via a Hoffmann code for X. Let H(X) be the entropy of X, then
  H(X) <= R(X) <= H(X) + 1
  H(X) = (sum Fi log2(n/Fi))/n and R(X) = (L.F)/n
Codes with memory : Codes which are not memory-less codes are codes with memory. These are the lossless codes for which its sometimes possible to achieve a compression rate below the entropy bound. 3 types
  Block codes : It partitions the data vector into blocks of given length, then each block is replaced by a code-word from a prefix set of binary words.
  Finite memory codes : Each data sample is encoded using a memoryless code from the code book which is determines by looking at a fixed number of previous data samples.
  Finite state code : It generalizes upon both the block codes and the finite memory codes.

## Slide 83: Run length encoding
A run-length code encodes the binary data-vector via encoding of the sequence of run lengths r1,r2,…,rk.
Notes: Useful for compression of binary data.
Conditional run length coding is another way in which run length coding can be implemented on a non-binary image.
  It involves a pre-coding step in which a binary code word is assigned adaptively to each pixel,
  followed by run length coding of the concatenated code words.
  The decomposition into bit planes is not used in conditional run length coding.

## Slide 84: Lossless coding Example Run length encoding
160 Blue,
3 Black,
8 Red,
3 Black,
8 White,
3 Black,
10 White,
3 Black,
12 Red,
3 Black,
8 White,
3 Black,
10 White,
3 Black,
4 Red,
3 Black,
40 Blue.
274 pixel wide
274 bytes
Numbers + colors
17(1) + 17(1) = 34 bytes
Compression ratio = 274÷34
 8:1

## Slide 85: Lossless Compression System
Original
Data (X)
Lossless
Encoder
Decoder
Decompressed Data = Original Data.
Original
Data (X)
Compressed
Data

## Slide 86: Lossy Compression Systems
Original
Data (X)
Lossy
Encoder
Decoder
Decompressed
Data (X’)
Compressed
Data
X’
Note: Decompressed Data  Original Data.

## Slide 87: JPEG

## Slide 88: Lossy coding (example)
Original Data :
Lossy encoding :
(Quantization)

## Slide 89: Frequency and Cycles Square Waves
Biological Psychology, Breedlove and Watson, 2013

## Slide 90: Frequency and Cycles Sine Waves
Biological Psychology, Breedlove and Watson, 2013

## Slide 91: DCT-based encoder
FDCT
Quantizer
Entropy
Encoder
Table
Specification
Table
Specification
8x8 blocks
Source
Image Data
Compressed
Image Data

## Slide 92: DCT-based decoder
Entropy
Decoder
Dequantizer
IDCT
Table
Specification
Table
Specification
Reconstructed
Image Data
Compressed
Image Data

## Slide 93: Square Wave using One Sine Wave
Sin(X)

## Slide 94: Square Wave using Two Sine Waves
Sin(X)+Sin(3x)

## Slide 95: Square Wave using Many Sine Waves
Sin(X)+Sin(3x)+Sin(5x)+Sin(7x)+...

## Slide 96: 2D DCT Functions
DC
DC + 1 AC
DC + 1 AC

## Slide 97: Discrete Cosine Transform JPEG

## Slide 98: Preparation for Entropy Coding
blocki-1
blocki
DCi-1
DCi
ΔDCi = DCi - DCi-1
Differential DC encoding
Zig-zag sequence
DC
AC01
AC07
AC77
AC70

## Slide 99: Example: Lenna Original

## Slide 100: Example: Lenna (DC)
0.19 bits/pixel

## Slide 101: Example: Lenna (DC + 1AC)
0.32 bits/pixel

## Slide 102: Example: Lenna (1DC + 2AC)
0.43 bits/pixel

## Slide 103: Example: Lenna (7msb DC)
0.15 bits/pixel

## Slide 104: Example: Lenna (7msb DC+7msb AC)
0.8 bits/pixel

## Slide 105: MPEG

## Slide 106: MPEG Video Coding Compression & Decompression
Preprocess
Motion
Compensation
DCT
Algorithm
Video
input
Compressed
Video
Reverse
Algorithm
Inverse
DCT
Filtering
& Processing
Compressed
Video
Video
Reverse
Motion Comp.
Compression
Decompression

## Slide 107: MPEG Video Coding Interframe coding
1
I
2
B
3
B
4
B
5
P
6
B
7
B
8
B
1
I
Bidirectional Prediction
Forward Prediction

## Slide 108: MPEG video coding procedure
I frame :
G
R
B
G
R
B
P/B frame :
Y
Cr
Cb
Y
Cr
Cb
Y
Cr
Cb
Reference frame(s)
01101100...
Transform coded
macroblock
Encoder output
+
+
-
+
110...
Input image
Input image
error terms
Transform coded
macroblock
YUV
conversion
YUV
conversion
Macroblock
Transform Coding
Entropy
Coding
Entropy
Coding
Transform
Coding of
Error
Terms
Motion vectors
Motion
compensation
(MPEG : Movie Picture Experts Groups)

## Slide 109: Motion JPEG & MPEG
A digital video sequence can be represented as a series of JPEG images.
In MPEG video, only the new (changed) parts of the video sequences need to be transmitted along with the information about the moving parts.
http://www.balooga.com/mpeg4.php3 A comparison of the encoding efficiencies..

## Slide 110: JPEG Video sequence
A three-picture JPEG video sequence
http://www.axis.com/documentation/whitepaper/video/video_compression.htm “Compression techniques,” White Paper – Axis .Communications

## Slide 111: MPEG Video sequence
A three-picture MPEG video sequence
http://www.axis.com/documentation/whitepaper/video/video_compression.htm “Compression techniques,” White Paper – Axis .Communications

## Slide 112: End